## Slide 1
CS:APP Chapter 4
Computer Architecture
Y86-64的顺序实现

## Slide 2: Y86-64 指令集#1
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9

## Slide 3: Y86-64 指令集#2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
7
0
cmovle
7
1
cmovl
7
2
cmove
7
3
cmovne
7
4
cmovge
7
5
cmovg
7
6

## Slide 4: Y86-64 指令集#3
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 5: Y86-64指令集#4
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 6: 构建的模块Building Blocks
组合逻辑
  输入值的布尔功能计算
  对输入变化连续响应
  操作数据并实现控制
存储部件
  存储位
  有地址的存储器
  无地址的寄存器
  只在时钟上升沿装载数据
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Clock
A
L
U
fun
A
B
MUX
0
1
=
Clock

## Slide 7: HCL硬件控制语言
  非常简单的硬件描述语言
    我们要研究和修改的部分
数据类型Data Types
  bool: Boolean
    a, b, c, …
  int: words
    A, B, C, …
    不指定字的大小---如是字节，64 位字等, …
声明
  bool a = bool-expr ;
  word A = int-expr ;

## Slide 8: HCL 操作
  按返回值的类型分类
布尔表达式
  逻辑操作
    a && b, a || b, !a
  字比较
    A == B, A != B, A < B, A <= B, A >= B, A > B
  集合成员
    A in { B, C, D }
      等同于：A == B || A == C || A == D
字表达式
  Case 表达式
    [ a : A; b : B; c : C ]
    按顺序依次测试表达式 a、b、c、...
    返回首次测试成功的值 A, B, C, …

## Slide 9: SEQ硬件结构
SEQ(sequential)处理器是Y86-64的顺序实现
状态
  程序计数器(PC)
  条件码寄存器(CC)
  寄存器文件
  内存
    访问相同的内存空间
    数据：用于读写程序数据
    指令：读指令
指令流
  按PC指示的地址读指令
  按每个阶段执行
  更新PC
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 10: SEQ 阶段
SEQ处理一条指令共分为六个阶段：
1、取指Fetch
  从内存读指令，地址为PC。取出内容有：
    第一个指令指示符字节的两个四位部分icode和ifun；
    第二个寄存器指示符字节rA和rB；（如果有）
    常数字valC；（如果有）
  计算下一条指令地址valP，即PC加已取指令的长度
2、译码Decode
  从寄存器读入最多两个操作数，得到值valA，valB（和/或)。通常是指令rA和rB字段指明的寄存器，有些指令读寄存器%rsp。

## Slide 11: SEQ 阶段
3、执行Execute
  ALU在执行阶段的计算有三种：
    指令ifun字段指明的操作
    计算内存引用的有效地址
    增加或减少指针
  计算结果为valE
  此阶段可能设置条件码
  对于条件传送指令：
    这个阶段会检验条件码和传送条件（ifun)，如果条件成立则更新目标寄存器
  对于跳转指令：
    这个阶段会决定是不是应该选择分支

## Slide 12: SEQ 阶段
4、访存Memory
  读写内存数据，读出的值为valM
5、写回Write Back
  最多写两个结果到寄存器文件
6、更新PC
  将PC设置为下一条指令的地址
处理器无限循环执行上述六个阶段。
在简化系统中，如果发生异常，处理器停止。停止的情况包括：执行halt指令、遇到非法指令、读写非法地址。
在复杂的完整设计中，如果发生异常，进入异常处理模式，执行由异常的类型决定的特殊代码。

## Slide 13: 指令译码
指令格式
  指令码字节 icode:ifun
  寄存器字节（可选） rA:rB
  常数字（可选） valC
5
0
rA
rB
D
icode
ifun
rA
rB
valC
Optional
Optional

## Slide 14: 执行算术/逻辑运算 6
Fetch
  读2个字节
Decode
  读操作数寄存器
Execute
  执行运算操作
  设置条件码
Memory
  什么都不做
Write back
  更新寄存器
PC Update
  PC加2
OPq rA, rB
6
fn
rA
rB

## Slide 15: 算术/逻辑运算中的各阶段计算
  指令的执行制定为按顺序的简单步骤
  对所有的指令使用相同的表格形式
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set condition code register
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 16: rmmovq指令的执行步骤 4
Fetch
  读10个字节
Decode
  读操作数寄存器
Execute
  计算有效地址
Memory
  写入存储器
Write back
  什么都不做
PC Update
  PC加10
rmmovq rA, D(rB)
4
0
rA
rB
D

## Slide 17: rmmovq的各阶段计算
  用ALU 计算地址
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
Read instruction byte
Read register byte
Read displacement D
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB + valC
Execute
Compute effective address
M8[valE]  valA
Memory
Write value to memory
Write
back
PC  valP
PC update
Update PC

## Slide 18: 跟踪第5行程序语句（rmmovq）的执行
rmmovq rA, D(rB)
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valC  M8[PC+2]
valP  PC+10
Fetch
valA  R[rA]
valB  R[rB]
Decode
valE  valB + valC
Execute
M8[valE]  valA
Memory
Write back
PC  valP
PC update
rmmovq %rsp, 100(%rbx)
icode:ifun  M1[0x20]=4:0
rA:rB  M1[0x21]=4:3
valC  M8[0x22]=100
valP 0x20+10=0x2a
valA 128
valB 12
valE 12+100=112
M[112] 128
PC0x2a
最终结果：
M[112] 128
PC0x2a

## Slide 19: popq指令的执行步骤
Fetch
  读2个字节
Decode
  读堆栈指针
Execute
  堆栈指针加8
Memory
  从旧的堆栈指针中读取数据
Write back
  更新堆栈指针
  向寄存器写入结果
PC Update
  PC+2
popq rA
b
0
rA
F

## Slide 20: popq的各阶段计算
  使用ALU实现堆栈指针加8
  必须更新两个寄存器
    一个用于弹出栈顶数据
    一个用于更新堆栈指针
popq rA
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[%rsp]
valB  R[%rsp]
Decode
Read stack pointer
Read stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read from stack
R[%rsp]  valE
R[rA]  valM
Write
back
Update stack pointer
Write back result
PC  valP
PC update
Update PC

## Slide 21
完成练习4.14

## Slide 22: 条件传送指令的执行步骤
Fetch
  读2个字节
Decode
  读操作数寄存器
Execute
  如果 !cnd, 设置目的寄存器为0xF
Memory
  什么都不做
Write back
  更新寄存器（或不更新）
PC Update
  PC+2
cmovXX rA, rB
2
fn
rA
rB

## Slide 23: 条件传送指令的各阶段计算
  寄存器rA的值通过ALU直送
  将目的寄存器置为0xF可取消传送
    如果条件代码和传送条件指示不传送
cmovXX rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
Compute next PC
valA  R[rA]
valB  0
Decode
Read operand A
valE  valB + valA
If ! Cond(CC,ifun) rB  0xF
Execute
Pass valA through ALU
(Disable register update)
Memory
R[rB]  valE
Write
back
Write back result
PC  valP
PC update
Update PC

## Slide 24: 跳转指令的执行步骤
Fetch
  读9个字节
  PC + 9
Decode
  什么也不做
Execute
  根据跳转的条件码决定是否执行分支
Memory
  什么也不做
Write back
  什么也不做
PC Update
  如果跳转到分支，PC置为Dest，否则PC加1
jXX Dest
7
fn
Dest
XX
XX
fall thru:
XX
XX
target:
Not taken
Taken

## Slide 25: 跳转指令的各阶段计算
  计算两个地址，然后根据分支条件选择
jXX Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Fall through address
Decode
Cnd  Cond(CC,ifun)
Execute
Take branch?
Memory
Write
back
PC  Cnd ? valC : valP
PC update
Update PC

## Slide 26: call指令的执行步骤
Fetch
  读9个字节
  PC + 9
Decode
  读栈指针
Execute
  栈指针减8
Memory
  将增加后的PC值写入新的栈指针值所指的栈单元
Write back
  更新栈指针
PC Update
  PC置为Dest
call Dest
8
0
Dest
XX
XX
return:
XX
XX
target:

## Slide 27: call指令的各阶段计算
  用 ALU完成栈指针的减8
  存储增加后的PC
call Dest
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
Fetch
Read instruction byte
Read destination address
Compute return point
valB  R[%rsp]
Decode
Read stack pointer
valE  valB + –8
Execute
Decrement stack pointer
M8[valE]  valP
Memory
Write return value on stack
R[%rsp]  valE
Write
back
Update stack pointer
PC  valC
PC update
Set PC to destination

## Slide 28: ret指令的执行步骤
Fetch
  读1个字节
Decode
  读栈指针
Execute
  栈指针加8
Memory
  从旧的栈指针中读出返回地址
Write back
  更新栈指针
PC Update
  PC 设置为返回值
ret
9
0
XX
XX
return:

## Slide 29: ret指令的各阶段计算
  用 ALU完成栈指针的加8
  从内存中读出返回值
ret
icode:ifun  M1[PC]
Fetch
Read instruction byte
valA  R[%rsp]
valB  R[%rsp]
Decode
Read operand stack pointer
Read operand stack pointer
valE  valB + 8
Execute
Increment stack pointer
valM  M8[valA]
Memory
Read return address
R[%rsp]  valE
Write
back
Update stack pointer
PC  valM
PC update
Set PC to return address

## Slide 30: 计算的步骤
  所有指令都遵循相同的一般模式，只是每个步骤的计算内容不同。
OPq rA, rB
icode:ifun  M1[PC]
rA:rB  M1[PC+1]
valP  PC+2
Fetch
Read instruction byte
Read register byte
[Read constant word]
Compute next PC
valA  R[rA]
valB  R[rB]
Decode
Read operand A
Read operand B
valE  valB OP valA
Set CC
Execute
Perform ALU operation
Set/use cond. code reg
Memory
[Memory read/write]
R[rB]  valE
Write
back
Write back ALU result
[Write back memory result]
PC  valP
PC update
Update PC
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC

## Slide 31: 计算的步骤
  所有指令都遵循相同的一般模式，只是每个步骤的计算内容不同。
call Dest
Fetch
Decode
Execute
Memory
Write
back
PC update
icode,ifun
rA,rB
valC
valP
valA, srcA
valB, srcB
valE
Cond code
valM
dstE
dstM
PC
icode:ifun  M1[PC]
valC  M8[PC+1]
valP  PC+9
valB  R[%rsp]
valE  valB + –8
M8[valE]  valP
R[%rsp]  valE
PC  valC
Read instruction byte
[Read register byte]
Read constant word
Compute next PC
[Read operand A]
Read operand B
Perform ALU operation
[Set /use cond. code reg]
Memory read/write
Write back ALU result
[Write back memory result]
Update PC

## Slide 32: 计算值
Fetch
  icode Instruction code
  ifun Instruction function
  rA Instr. Register A
  rB Instr. Register B
  valC Instruction constant
  valP Incremented PC
Decode
  srcA Register ID A
  srcB Register ID B
  dstE Destination Register E
  dstM Destination Register M
  valA Register value A
  valB Register value B
Execute
  valE ALU result
  Cnd Branch/move flag
Memory
  valM Value from memory

## Slide 33: SEQ硬件
画图惯例（图4-23）：
蓝框: 预设计好的硬件模块
    如内存, ALU
  灰框: 控制逻辑，从一组信号源中选择或计算布尔函数
    用HCL描述
  白色椭圆框: 线路标识（非部件）
  粗线: 64-bit字值
  细线: 4-8 bit 值
  虚线: 1位值

## Slide 34: SEQ的时序
原则：从不回读
处理器从来不需要为了完成一条指令的执行而去读由该指令更新了的状态。

## Slide 35: SEQ 操作
状态逻辑
  PC 寄存器
  Cond. Code寄存器
  Data 存储器
  寄存器文件
  均在时钟上升沿更新
组合逻辑
  ALU
  控制逻辑 存储器读
    指令存储器
    寄存器文件
    数据存储器
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
Read
Write

## Slide 36: SEQ 操作 #2
  状态为第2条irmovq指令的状态
  组合逻辑开始对状态变化做出反应
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
Read
Write

## Slide 37: SEQ Operation #3
  状态为第2条irmovq指令的状态
  组合逻辑产生addq指令的结果
Combinational
logic
Data
memory
Register
file
%rbx = 0x100
PC
0x014
CC
100
Read
ports
Write
ports
0x016
000
%rbx
<--
0x300
Read
Write
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write

## Slide 38: SEQ Operation #4
  状态为addq指令的状态
  组合逻辑开始对状态变化做出反应
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
Read
Write

## Slide 39: SEQ Operation #5
  状态为addq指令的状态
  组合逻辑产生je指令的结果
0x014: addq %rdx,%rbx # %rbx <-- 0x300 CC <-- 000
0x016: je dest # Not taken
0x01f: rmmovq %rbx,0(%rdx) # M[0x200] <-- 0x300
Cycle 3:
Cycle 4:
Cycle 5:
0x00a: irmovq $0x200,%rdx # %rdx <-- 0x200
Cycle 2:
0x000: irmovq $0x100,%rbx # %rbx <-- 0x100
Cycle 1:
Clock
Cycle 1
j
l
m
k
Cycle 2
Cycle 3
Cycle 4
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write
Combinational
logic
Data
memory
Register
file
%rbx = 0x300
PC
0x016
CC
000
Read
ports
Write
ports
0x01f
Read
Write

## Slide 40: SEQ各阶段的实现
HCL描述中使用的常数值

## Slide 41: 1、Fetch取指阶段
预定义的模块
  PC: 装有PC的寄存器
  Instruction memory: 读10个字节 (PC to PC+9)
    Signal invalid address
  Split: 把指令字节分到icode 和 ifun
  Align: 取字段放入rA, rB, 和 valC
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-9
Byte 0
imem_error
icode
ifun

## Slide 42: Fetch 的逻辑
控制逻辑
Instr_Valid: 指令合法吗?
  icode, ifun: 如果指令地址不合法则产生nop指令
  Need_regids: 这个指令包括一个寄存器指示符字节吗?
  Need_valC：这个指令包括一个常数字吗?
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-9
Byte 0
imem_error
icode
ifun

## Slide 43: HCL表达的Fetch控制逻辑
# Determine instruction code
int icode = [
imem_error: INOP;
1: imem_icode;
];
# Determine instruction function
int ifun = [
imem_error: FNONE;
1: imem_ifun;
];
Instruction
memory
PC
Split
Byte 0
imem_error
icode
ifun

## Slide 44: HCL表达的Fetch控制逻辑
bool need_regids =
icode in { IRRMOVQ, IOPQ, IPUSHQ, IPOPQ,
IIRMOVQ, IRMMOVQ, IMRMOVQ };
bool instr_valid = icode in
{ INOP, IHALT, IRRMOVQ, IIRMOVQ, IRMMOVQ, IMRMOVQ,
IOPQ, IJXX, ICALL, IRET, IPUSHQ, IPOPQ };
push rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
8
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
Instr
valid
Need
regids

## Slide 45
练习4.19：写出need_valC的HCL代码。
bool need_valC =
icode in { IIRMOVQ, IRMMOVQ, IMRMOVQ, IJXX, ICALL };
Instruction
memory
PC
increment
rB
icode
ifun
rA
PC
valC
valP
Need
regids
Need
valC
Instr
valid
Align
Split
Bytes 1-9
Byte 0
imem_error
icode
ifun

## Slide 46: 2、译码(decode)和写回(write back)阶段
Register File
  读端口 A, B
  写端口 E, M
  地址是寄存器IDs 或 15 (0xF) (不可达)
控制逻辑
  srcA, srcB:读取端口地址
  dstE, dstM:写入端口地址
rB
dstE
dstM
srcA
srcB
Register
file
A
B
M
E
dstE
dstM
srcA
srcB
icode
rA
valB
valA
valE
valM
Cnd
信号
  Cnd:指示是否执行有条件mov
    在执行阶段计算

## Slide 47: srcA
int srcA = [
icode in { IRRMOVQ, IRMMOVQ, IOPQ, IPUSHQ } : rA;
icode in { IPOPQ, IRET } : RRSP;
1 : RNONE; # Don't need register
];
cmovXX rA, rB
valA  R[rA]
Decode
Read operand A
rmmovq rA, D(rB)
valA  R[rA]
Decode
Read operand A
popq rA
valA  R[%rsp]
Decode
Read stack pointer
pushq rA
Decode
Read operand A
call Dest
valA  R[%rsp]
Decode
Read stack pointer
ret
Decode
No operand
OPq rA, rB
valA  R[rA]
Decode
Read operand A
srcA
注：有部分指令图中未画出

## Slide 48: dstE
int dstE = [
icode in { IRRMOVQ } && Cnd : rB;
icode in { IIRMOVQ, IOPQ} : rB;
icode in { IPUSHQ, IPOPQ, ICALL, IRET } : RRSP;
1 : RNONE; # Don't write any register
];
None
R[%rsp]  valE
Update stack pointer
None
R[rB]  valE
cmovXX rA, rB
Write-back
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Write-back
Write-back
Write-back
Write-back
Write-back
Conditionally write back result
R[%rsp]  valE
Update stack pointer
R[%rsp]  valE
Update stack pointer
R[rB]  valE
OPq rA, rB
Write-back
Write back result
Update stack pointer
pushq rA
R[%rsp]←valE
Write-back
dstE
注：有部分指令图中未画出，如irmovq

## Slide 49
练习：写出srcB和desM的HCL代码。
rB
dstE
dstM
srcA
srcB
Register
file
A
B
M
E
dstE
dstM
srcA
srcB
icode
rA
valB
valA
valE
valM
Cnd
word srcB = [
icode in { IOPQ, IRMMOVQ, IMRMOVQ } : rB;
icode in { IPUSHQ, IPOPQ, ICALL, IRET } : RRSP;
1 : RNONE; # Don't need register
];
word dstM = [
icode in { IMRMOVQ, IPOPQ } : rA;
1 : RNONE; # Don't write any register
];

## Slide 50: Execute执行阶段
单元
  ALU
    实现 4 项功能 生成条件代码值cc 有3位的条件码寄存器
  cond
    计算条件转移/传送标志
控制逻辑
  Set CC: 是否加载条件码寄存器？
  ALU A: 输入 A 到 ALU
  ALU B: 输入 B 到 ALU
  ALU fun: ALU 执行什么计算功能?
CC
ALU
ALU
A
ALU
B
ALU
fun.
Cnd
icode
ifun
valC
valB
valA
valE
Set
CC
cond

## Slide 51: ALU A 输入
word aluA = [
icode in { IRRMOVQ, IOPQ } : valA;
icode in { IIRMOVQ, IRMMOVQ, IMRMOVQ } : valC;
icode in { ICALL, IPUSHQ } : -8;
icode in { IRET, IPOPQ } : 8;
# Other instructions don't need ALU
];
valE  valB + –8
Decrement stack pointer
No operation
valE  valB + 8
Increment stack pointer
valE  valB + valC
Compute effective address
valE  0 + valA
Pass valA through ALU
cmovXX rA, rB
Execute
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 8
Increment stack pointer
valE  valB OP valA
Perform ALU operation
OPq rA, rB
Execute
ALU
A
注：有部分指令图中未画出，如irmovq,mrmovq,pushq

## Slide 52: ALU 运算
word alufun = [
icode == IOPQ : ifun;
1 : ALUADD;
];
valE  valB + –8
Decrement stack pointer
No operation
valE  valB + 8
Increment stack pointer
valE  valB + valC
Compute effective address
valE  0 + valA
Pass valA through ALU
cmovXX rA, rB
Execute
rmmovl rA, D(rB)
popq rA
jXX Dest
call Dest
ret
Execute
Execute
Execute
Execute
Execute
valE  valB + 8
Increment stack pointer
valE  valB OP valA
Perform ALU operation
OPq rA, rB
Execute
ALU
fun.

## Slide 53: set_CC
所有指令中，只有OPq指令时才设置条件码。
set_cc是用于控制是否应该更新条件码寄存器。
bool set_cc = icode in { IOPQ };

## Slide 54
练习4.23 写出信号aluB的HCL描述。
CC
ALU
ALU
A
ALU
B
ALU
fun.
Cnd
icode
ifun
valC
valB
valA
valE
Set
CC
cond
word aluB = [
icode in { IRMMOVQ, IMRMOVQ, IOPQ, ICALL,
IPUSHQ, IRET, IPOPQ } : valB;
icode in { IRRMOVQ, IIRMOVQ } : 0;
# Other instructions don't need ALU
];

## Slide 55: Memory访存阶段
存储器
  读写内存字
控制逻辑
  stat: 指令状态是什么?
  Mem_read: 字是否可读?
  Mem_write: 字是否可写?
  Mem_addr: 选择地址
  Mem_data: 选择数据
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat

## Slide 56: stat指令状态
控制逻辑
  stat: 指令状态是什么?
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat
## Determine instruction status
int Stat = [
imem_error || dmem_error : SADR;
!instr_valid: SINS;
icode == IHALT : SHLT;
1 : SAOK;
];

## Slide 57: Mem_addr存储器地址
OPq rA, rB
Memory
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
No operation
M8[valE]  valA
Memory
Write value to memory
valM  M8[valA]
Memory
Read from stack
M8[valE]  valP
Memory
Write return value on stack
valM  M8[valA]
Memory
Read return address
Memory
No operation
int mem_addr = [
icode in { IRMMOVQ, IPUSHQ, ICALL, IMRMOVQ } : valE;
icode in { IPOPQ, IRET } : valA;
# Other instructions don't need address
];
注：有部分指令图中未画出，如irmovq,mrmovq,pushq

## Slide 58: Mem_read存储器读取
OPq rA, rB
Memory
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
No operation
M8[valE]  valA
Memory
Write value to memory
valM  M8[valA]
Memory
Read from stack
M8[valE]  valP
Memory
Write return value on stack
valM  M8[valA]
Memory
Read return address
Memory
No operation
bool mem_read = icode in { IMRMOVQ, IPOPQ, IRET };
注：有部分指令图中未画出，如mrmovq

## Slide 59
练习4.23 写出信号mem_data和mem_write的HCL描述。
Data
memory
Mem.
read
Mem.
addr
read
write
data out
Mem.
data
valE
valM
valA
valP
Mem.
write
data in
icode
Stat
dmem_error
instr_valid
imem_error
stat
word mem_data = [
icode in { IRMMOVQ, IPUSHQ } : valA;
icode == ICALL : valP;
# Default: Don't write anything
];
bool mem_write = icode in { IRMMOVQ, IPUSHQ, ICALL };

## Slide 60: PC更新阶段
New PC
  选择 PC 的下一个值
New
PC
Cnd
icode
valC
valP
valM
PC

## Slide 61: PC更新
OPq rA, rB
rmmovq rA, D(rB)
popq rA
jXX Dest
call Dest
ret
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  valP
PC update
Update PC
PC  Cnd ? valC : valP
PC update
Update PC
PC  valC
PC update
Set PC to destination
PC  valM
PC update
Set PC to return address
int new_pc = [
icode == ICALL : valC;
icode == IJXX && Cnd : valC;
icode == IRET : valM;
1 : valP;
];

## Slide 62: SEQ总结
实现
  将每个指令作为一系列简单的步骤表达 每个指令类型遵循相同的一般流程
  将寄存器、存储器、预设计的组合部件汇集在一起
  用组合逻辑连接
局限性
  太慢了，不实用 在一个时钟周期中，必须通过指令存储器、注册文件、ALU 和数据存储器传播 需要运行时钟非常缓慢
  硬件单元仅在时钟周期的一小部分处于活动状态